## Slide 1: Capstone Meeting
1/25/2018

## Slide 2: 3D detection
3D detection v.s. 2D detection
  RGB-D(2.5D)/RGB, geometric data(3D) v.s. RGB data
  3D position/orientation v.s. 2D position
Detection pipeline
  Region proposal
  (detection)
  Classifier
  (recognition)
Region proposal
Object
classification
Notes: Recently years, there are great successes in the field of 2D detection. There are some similarities and discrepancies between 2D and 3D detection which are mostly caused by rise of dimension. For example, in 3D detection, we take both RGB and 3D or 2.5D data as input and predict 3D position as well as orientation of interested objects while, in 2D detection, we only take RGB as input data and only interested in 2D positions. Recent works on detection basically share a common hierarchy pipeline: region proposals for objectness area and a classifier built upon those proposals for recognition.

## Slide 3: 3D detection
3D detection benchmark
  7481 training images and 7518 test images/point clouds/80256 labeled objects
Notes: One of the most popular 3D detection benchmark is Kitti which contains 7481 training images, 7518 test images with corresponding point cloud, comprising a total of 80256 objects.

## Slide 4: State-of-the-arts on Kitti 3D detection
Point Cloud Understanding
  Frustum-PointNet
  VoxelNet
Multimodal Fusion Methods
  AVOD
  SqueezeSeg
  MV3D
  PointFusion
Notes: Several methods are proposed for kitti 3D detection challenge and here are some of the top methods that I roughly separate into two categories: methods based on point cloud understanding and multimodal fusion methods. I will, from my understanding, briefly cover the ideas of those papers.

## Slide 5: Frustum-pointnet
Hierarchical architecture
  Fast-rcnn for 2d detection
  2d bbox -> 3d frustum using depth
  3d segmentation & 3d box regression using pointnet
Notes: This paper proposed a hierarchical pipeline for 3D detection using both RGB data and corresponding point cloud. There are 3 stages. In the first stage, they utilize off the shell method like faster-rcnn to get 2d proposals/detection. Then the 2D bbox are lifted to a frustum given the camera intrinsic and extrinsic.

## Slide 6: Frustum-pointnet
3D instance segmentation
  Binary classification per point
3D box estimation
  Distance between predicted and GT corners
Classification Loss (recognition)
Both classification &
Regression Loss
(localization)
Joint optimization for box parameters
Notes: In the second stage, instance segmentation is performed on the points in that frustum and finally a pointnet is introduced to regress the parameters of 3D boxes from points which are labeled as object.

## Slide 7: Frustum-pointnet
Shortcomings
  Strong reliance on 2D detection results
  Using only semantics information(RGB) on extracting region proposals
Notes: One of the main drawbacks of f-pointnet is that once the 2D detection failed, the whole pipeline are not able to work. And it only considers semantic information on generating proposals.

## Slide 8: VoxelNet
Hierarchical architecture(only Lidar point)
  Encode dense point clouds into sparse voxel-wise feature
  Perform 3D box regression upon that feature using CNN
Notes: The second method in this class is voxelnet. The main features of this method are that it only use lidar data as input and this method is very fast. Unlike f-pointnet, voxelnet directly generate 3D proposals from raw point cloud.

## Slide 9: VoxelNet
Pointwise feature->voxel feature
3D box regression +
binary classification
Sparse tensor
Notes: More specifically, voxelnet first separate the whole space evenly into grids and adopt a pointnet to learn feature for each bin. In this way, point-wise features are transferred into voxelized features which are more compact. Then a conventional CNN is applied to perform 3D box regression on voxelized features. Despite those improvements on algorithm, they implemented a sparse tensor representation from engineering aspect which greatly accelerate the whole procedure.

## Slide 10: VoxelNet
Shortcomings
  Misalignment of voxels -> fractions
  No attention module
Notes: The main drawbacks come from two folds. First, misalignment is inevitable in their method and might cause fractions of objects and further jeopardize the intrinsic structure of interested objects. On the other hand, more efficient learning method for proposal generating using point cloud is still remained to be proposed.

## Slide 11: Multimodal Late Fusion
MV3D (RGB+FV+BV)
AVOD (RGB+BEV)
PointFusion (RGB+point cloud)
Notes: Except for the first class of method, there are some methods based on multimodal learning. These method all use a multi-channel CNN or neural network as backbone for 3D detection.

## Slide 12: MV3D
Inputs:
  RGB
  front view
  bird view
Notes: This is one of the early work. They take RGB, front view depth geometric data and bird view data as inputs.

## Slide 13: MV3D
Deep fusion
  Fusion at each layer
  Modal specific regularization
Notes: And they proposed a deep fuse architecture to utilize the information from different modalities and preserve individual property in different channels by weights sharing between deep fuse network and modal-specific network that performs the same task.

## Slide 14: AVOD
Naïve late fusion + NMS
Notes: In some recent works like AVOD, are very similar to MV3D, but achieve better performance on kitti.

## Slide 15: PointFusion
Global + point-wise feature

## Slide 16: Multimodal Late Fusion
MV3D
AVOD
PointFusion

## Slide 17
Detection
  Efficient search in large 3D point cloud using selective search/inference (VoxelNet)
  How to incorporate geometric information to help 2D detection or use geometric information as feedback(f-pointnet) for region proposal.
Recognition
  Multimodal learning
  Efficient model for point cloud understanding(kd-network, O-CNN, point supergraph, pointnet++)
  How to recognize occluded or deformed point cloud models
  2.5D->3D point cloud completion (inferring invisible points from perspective point cloud)
Notes: There are some possible directions we can go.

## Slide 18: RGB-D Object Recognition using Multi-modal Learning

## Slide 19: Project Introduction
Goal
  RGB-D Object Recognition
  Better Feature Representation
  fully Utilize Multi-Modal Information
Method
  Multi-Modal learning
  Representation learning
Notes: In this RGB-D object recognition project, our goal is to design a better feature representation for RGB-D objects by leveraging the multi-modal information from RGB and depth channel. In 2D visions, RGB can provide us with many information like color or texture while the information along the projection axis is missing. So RGB image solo can give rise to confusions and using depth as a complimentary for RGB image will definitely improve object recognition. However there are some shareable part in both RGB and depth, for instance shape. Thus simply combine the feature of RGB and depth is not wise which might cause the misuse of features from different modality. So we proposed a multi-modal deep learning algorithm for RGB-D object recognition.

## Slide 20: Project Introduction
Two-Stream CNN
  Feature extraction
CIM Layer
  Semi-supervised Training
  Objectives
Notes: What we do is to first implement a two stream convolutional neural network for RGB and Depth feature extraction.
Then we designed a CIM layer to generate better feature for RGB-D object by analyzing the correlated part as well as individual part of RGB and depth feature extracted. To generate a more powerful feature presentation, we come up with a cost function which can learn the mapping matrices of correlated space and individual space. To force the similarity between correlated part extracted from both modalities, we reduce L2 distance between those correlated parts. Additionally, two regularization terms are added to prevent information loss and retain modal specific information. Then we can get a more explicit expression of multi-modal feature by concatenating correlated part and individual part.

## Slide 21: Project Introduction
Tested on two RGB-D object recognition datasets
  Results on RGB-D Object Dataset
Notes: We tested our method on two datasets and, at that time, outperformed most of those works under the same experimental settings.

## Slide 22: Project Introduction
Tested on two RGB-D object recognition datasets
  Results on 2D3D Dataset

## Slide 23: Project Introduction
Parameter Evaluation
  Manually Tuned Ratios V.S. learnt Ratios
P stands for the weight of correlated part
Notes: We also tested on effectiveness of various weights of different part of our feature.
In this section, we manually set the weight of correlated part and individual part of
the two features while in our proposed methods we learn our weight in training period.
And we get the same weight for the peak accuracy in both experiments.

## Slide 24: AVOD

## Slide 25: PointFusion

## Slide 26: SqueezeSeg
Encode point cloud into

## Slide 27: PointNet++
Goal
  Point set understanding
  Classification
  segmentation
Innovations
  Hierarchical feature learning
  Structural input
Notes: This is an incremental work of pointnet. The goal of this paper is still on point set understanding, but they emphasis more on the structure of a point set and proposed a hierarchical feature learning pipeline to encode the spatial information of a point set.

## Slide 28: PointNet++
Basic modules
  Sampling layer
    farthest point sampling
  Grouping layer
    Ball query
  PointNet layer
    Feature generation
  Point Feature Propagation
    Feature interpolation using
    K nearest neighbors
Notes: Be more specific, pointnet++ has three basic parts. The first one is sampling layer which selects a subset of the whole point set as centroids. In this layer, they use farthest point sampling to better cover the whole set. Then, given those K centroids, the whole part is grouped into K subsets using ball query. Finally, pointnet is applied to learn a feature representation for each of those K groups.
For pointset classification, a fully connected layer is applied as a classifier. For segmentation, feature interpolation for each points is performed for upscaling.

## Slide 29: PointNet++
density adaptive PointNet layer
  Multi-scale grouping (MSG)
  Multi-resolution grouping (MRG)
Notes: Considering that points are not evenly distributed and some area might have a higher density while some area might have a low density, they embed features from different scales and different resolutions.

## Slide 30: 3D detection
3D detection v.s. 2D detection
  RGB-D(2.5D)/RGB, geometric data(3D) v.s. RGB data
  3D position/orientation v.s. 2D position
Detection pipeline
  Region proposal
  (detection)
  Classifier
  (recognition)
Region proposal
Object
classification
Notes: Recently years, there are great successes in the field of 2D detection. There are some similarities and discrepancies between 2D and 3D detection which are mostly caused by rise of dimension. For example, in 3D detection, we take both RGB and 3D or 2.5D data as input and predict 3D position as well as orientation of interested objects while, in 2D detection, we only take RGB as input data and only interested in 2D positions. Recent works on detection basically share a common hierarchy pipeline: region proposals for objectness area and a classifier built upon those proposals for recognition.

## Slide 31: 3D detection
3D detection benchmark
  7481 training images and 7518 test images/point clouds/80256 labeled objects
Notes: One of the most popular 3D detection benchmark is Kitti which contains 7481 training images, 7518 test images with corresponding point cloud, comprising a total of 80256 objects.

## Slide 32: State-of-the-arts on Kitti 3D detection
Point Cloud Understanding
  Frustum-PointNet
  VoxelNet
Multimodal Fusion Methods
  AVOD
  SqueezeSeg
  MV3D
  PointFusion
Notes: Several methods are proposed for kitti 3D detection challenge and here are some of the top methods that I roughly separate into two categories: methods based on point cloud understanding and multimodal fusion methods. I will, from my understanding, briefly cover the ideas of those papers.

## Slide 33: Frustum-pointnet
Hierarchical architecture
  Fast-rcnn for 2d detection
  2d bbox -> 3d frustum using depth
  3d segmentation & 3d box regression using pointnet
Notes: This paper proposed a hierarchical pipeline for 3D detection using both RGB data and corresponding point cloud. There are 3 stages. In the first stage, they utilize off the shell method like faster-rcnn to get 2d proposals/detection. Then the 2D bbox are lifted to a frustum given the camera intrinsic and extrinsic.

## Slide 34: Frustum-pointnet
3D instance segmentation
  Binary classification per point
3D box estimation
  Distance between predicted and GT corners
Classification Loss (recognition)
Both classification &
Regression Loss
(localization)
Joint optimization for box parameters
Notes: In the second stage, instance segmentation is performed on the points in that frustum and finally a pointnet is introduced to regress the parameters of 3D boxes from points which are labeled as object.

## Slide 35: Frustum-pointnet
Shortcomings
  Strong reliance on 2D detection results
  Using only semantics information(RGB) on extracting region proposals
Notes: One of the main drawbacks of f-pointnet is that once the 2D detection failed, the whole pipeline are not able to work. And it only considers semantic information on generating proposals.

## Slide 36: VoxelNet
Hierarchical architecture(only Lidar point)
  Encode dense point clouds into sparse voxel-wise feature
  Perform 3D box regression upon that feature using CNN
Notes: The second method in this class is voxelnet. The main features of this method are that it only use lidar data as input and this method is very fast. Unlike f-pointnet, voxelnet directly generate 3D proposals from raw point cloud.

## Slide 37: VoxelNet
Pointwise feature->voxel feature
3D box regression +
binary classification
Sparse tensor
Notes: More specifically, voxelnet first separate the whole space evenly into grids and adopt a pointnet to learn feature for each bin. In this way, point-wise features are transferred into voxelized features which are more compact. Then a conventional CNN is applied to perform 3D box regression on voxelized features. Despite those improvements on algorithm, they implemented a sparse tensor representation from engineering aspect which greatly accelerate the whole procedure.

## Slide 38: VoxelNet
Shortcomings
  Misalignment of voxels -> fractions
  No attention module
Notes: The main drawbacks come from two folds. First, misalignment is inevitable in their method and might cause fractions of objects and further jeopardize the intrinsic structure of interested objects. On the other hand, more efficient learning method for proposal generating using point cloud is still remained to be proposed.